## Slide 1: Nonlinear Optics Study CH-1 Boyd, R. W. Nonlinear optics (4th ed.)
Kyungmin Kwon

## Slide 2: 1.1 Introduction to Nonlinear Optics

## Slide 3: Introduction
Nonlinear Optics
The study of phenomena that occur as a consequence of the modification of the optical properties of a material system by the presence of light
When the response of a material system to an applied optical field depends in a nonlinear manner on the strength of the applied optical system
Laser light is sufficiently intense to modify the optical properties of a material system
Meaning of “Nonlinear”
Polarization (the dipole moment per unit volume of a material system)
In order to describe more precisely what we mean by an optical nonlinearity,
: linear susceptibility
: permittivity of free space

## Slide 4: Optical Response for Nonlinear Optics
As a power series in the field strength
: second-rank tensor, third-rank tensor (the fields are vectors)
Assumption
The polarization at time depends only on the instantaneous value of the electric field strength
The medium must be lossless and dispersionless
In general, the nonlinear susceptibilities depend on the frequencies of the applied fields
Our assumption gives them to be constants
Kramers-Kronig relations
Dirac-delta function

## Slide 5: Optical Response for Nonlinear Optics
Polarization : Act as the source of new components of the electromagnetic field
: linear refractive index
: the speed of light in vacuum
Inhomogeneous wave equation in which the polarization acts as a source term for the E-field
A measure of the acceleration of the charges that constitute the medium
Consistent with Larmor’s theorem of Electromagnetism
(accelerated charges generate electromagnetic radiation)

## Slide 6: 1.2 Descriptions of Nonlinear Optical Processes

## Slide 7: Second Harmonic Generation
It is incident upon a crystal for which the second-order susceptibility is nonzero
Electric field strength of a laser beam in lossless medium
A contribution at zero frequency
A contribution at
Optical rectification : static electric field is created across the nonlinear crystal
Driven Wave Equation
The generation of radiation at

## Slide 8: Second Harmonic Generation (cont.)
Nearly all of the power in the incident beam at is converted into radiation at the second-harmonic frequency
Second-harmonic generation under experimental condition
One common use of SHG is to convert the output of a fixed-frequency laser to a different spectral region
Nd:YAG laser (infrared @ ) → to convert (middile of visible spectrum @ )
Interaction in terms of the exchange of photons between the various frequencies of the field.
A single quantum-mechanical process
Two photon () : destroyed, a photon () : simultaneously created
Solid line : the atomic ground state
Dashed line : virtual level
Not energy eigenlevels of the free atom
Combined energy of the atom and of one or more photons of radiation

## Slide 9: Sum and Difference-Frequency Generation
Two distinct frequency components
Optical field incident upon a second-order nonlinear optical medium
Nonlinear polarization
The summation extends over positive and negative frequencies

## Slide 10: Sum and Difference-Frequency Generation (cont.)
The complex amplitudes of the various frequencies of the nonlinear polarizations
Labeling each terms with
Response at the negative frequency components
SHG
SHG
SFG
DFG
OR
SHG
SHG
SFG
DFG

## Slide 11: Phase-matching
Introduction to phase-matching condition
Four different nonzero frequency components
SHG
SHG
SFG
DFG
OR
Typically, no more than one of four frequency components are present in the nonlinear polarization
The nonlinear polarization can efficiently produce an output signal only if a certain phase-matching condition is satisfied
Usually this condition cannot be satisfied for more than one frequency component of the nonlinear polarization
Radiated frequencies are selected via input polarization and crystal orientation

## Slide 12: Sum-Frequency Generation
The process of SFG
To produce : tunable radiation @ ultraviolet region
Application of SFG
SFG is analogous to that of SHG, except that in SFG the two input waves are at different frequencies
Choosing the input waves : fixed frequency laser and frequency-tunable laser @ visible region

## Slide 13: Difference-Frequency Generation
The process of DFG
To produce : tunable radiation @ infrared region
Application of DFG
DFG and SFG appear to be very similar processes
By choosing the input waves : fixed frequency laser and frequency-tunable laser @ visible region

## Slide 14: Optical parametric amplification
Difference between SFG and DFG
Conservation of energy
Photon () : A photon () is destroyed and a photon () is created
: created
: destroyed
: destroyed
: destroyed
The lower-frequency input field is amplified by the process of DFG
Optical parametric amplification
The atom first absorbs a photon of frequency and jumps to the highest virtual level
This level decays by a two-photon emission process that is stimulated by the field
If the absence of the field?
DFG

## Slide 15: Optical parametric amplification

## Slide 16: Spontaneous Parametric Down Conversion
The absence of E-field
Even if the field is not applied, two-photon emission can occur.
In such a case, the generated fields are very much weaker
: created
: destroyed
They are created by spontaneous two-photon emission from a virtual level
Spontaneous parametric down-conversion or Parametric fluorescence

## Slide 17: Optical Parametric Oscillation
In the process of DFG that the presence of radiation at or can stimulate the emission of photon
If the nonlinear crystal used in this process is placed inside an optical resonator,
A device is broadly tunable because of their extremely broad tuning range
Controlling output frequency of an optical parametric oscillator by adjusting phase-matching condition
Optical Parametric Oscillator
or Fields can build up to large values
In practical,
The applied field frequency : pump frequency
The desired output frequency : signal frequency ; The unwanted output frequency : idler frequency

## Slide 18: Third-Order Nonlinear Optical Processes
Third order contribution to the nonlinear polarization
Generally, the E-field is made up of several different frequency components
But it is very complicated, so we first consider monochromatic applied field
Third-harmonic generation
Three photons are destroyed
One photon is created

## Slide 19: Intensity-Dependent Refractive Index
Nonlinear contribution to the refractive index
The refractive index in the presence of this type of nonlinearity
Optical constant in lossless medium
: usual (linear or low-intensity) refractive index
: the intensity of incident wave

## Slide 20: Self Focusing
If intensity-dependent refractive index is Self-Focusing
The process can occur when a beam of light having a nonuniform transverse intensity distribution propagates through a material for which is positive
the material effectively acts as a positive lens
The intensity at the focal spot of the self focused beam is usually sufficiently large to lead to optical damage of the material

## Slide 21: Third-Order Interactions (General Case)
Nonlinear polarization consists of three frequency components
When calculating , we find 44 different frequency components (considering positive and negative frequencies)

## Slide 22: Third-Order Interactions (General Case)
Again representing the nonlinear polarization
Distinct permutation

## Slide 23: Parametric versus Nonparametric Processes
Parametric
In a parametric process, population can be removed from the ground state only for those brief intervals of time when it resides in a virtual level
Parametric : a process in which the initial and final quantum-mechanical states of the system are identical
By uncertainty principle, population can reside in a virtual level for a time interval
: energy difference between the virtual level and the nearest real level
Nonparametric
Processes that do involve the transfer of population from one real level to another

## Slide 24: Parametric versus Nonparametric Processes
Parametric vs Nonparametric
Nonparametric : described by a complex susceptibility
Parametric : always be described by a real susceptibility
Parametric : Photon energy is always conserved.
Because energy can be transferred to or from the material medium
Nonparametric : Photon energy need not be conserved
Example of parametric vs nonparametric
Parametric : real part of the refractive index
Nonparametric : imaginary part of the refractive index describes the absorption of radiation
It results from the transfer of population from the atomic ground state to an excited state

## Slide 25: Saturable Absorption
Saturable Absorption
Many material systems : absorption coefficient decreases when the laser intensity is high
: low-intensity absorption coefficient
: saturation intensity
Absorption Coefficient

## Slide 26: Saturable Absorption
Optical Bistability
Bistable optical device : a saturable absorber inside a Fabry-Perot resonator
Input intensity ↑ → field in the cavity ↑ → absorption ↓ → field intensity ↑
Subsequently, if input intensity is lowered, the field intensity tends to remain large
Absorption of the material system has already been reduced (saturated)
Over some range of input intensities more than one output intensity is possible

## Slide 27: Two Photon Absorption
Two photon absorption
An atom makes a transition from its ground state to an excited state by the simultaneous absorption of two laser photons
Absorption cross section : the total area of incident beam is scattered by the target
: coefficient that describes strength of the two-photon-absorption process
Atomic transition rate
Application : spectroscopic tool for determining the positions of energy levels that are not connected to the atomic ground state by a one-photon transition
In linear optics, is a constant

## Slide 28: Stimulated Raman Scattering
Stimulated Raman Scattering
A photon () is annihilated and a photon at the Stokes-shifted frequency is created
The efficiency of stimulated Raman scattering can be quite large or more of the power
The efficiency of normal or spontaneous Raman scattering is many orders of magnitude lower
Other stimulated scattering processes also occur. (Brillouin, Rayleigh scattering)
Leaving the molecule (or atom) in an excited state with energy
Vibrational energy

## Slide 29: 1.3 Formal Definition of the Nonlinear Susceptibility

## Slide 30: E-field of the Frequency Components
General case of a material with dispersion and/or absorption
Assuming the E-field vector as the discrete sum of a number of frequency components
Nonlinear susceptibility : a complex quantity
Assuming that to define the spatially slowly varying field amplitude
Summation over positive frequency
Rewrite the total field

## Slide 31: E-field of the Frequency Components (cont.)
General case of a material with dispersion and/or absorption
Definition of field amplitude
Or alternatively, by the slowly varying amplitude
The nonlinear polarization

## Slide 32: Second-order Nonlinear Polarization
Define the components of the second-order susceptibility tensor (constant)
Nonlinear polarization is proportional to second-order susceptibility tensor
: Cartesian components of the fields
: Summation over
: Nonlinear polarization oscillates at
: sometimes written as because
Let’s examine two simple examples

## Slide 33: Sum Frequency Generation
SFG :
: dummy indices, they can be interchanged
Assuming that the nonlinear susceptibility possesses intrinsic permutation symmetry
For the special case, both input fields are polarized in the direction

## Slide 34: Sum Harmonic Generation
SHG : input frequency as ,
Assuming both input fields are polarized in the direction
About a factor of 2
SFG
SHG
As goes , must approach in SFG
Why doesn’t the factor of 2 appear at first in the SHG expression? Because our susceptibility convention lists each input frequency in an ordered permutation
Someone thought : “polarization produced by two distinct fields is larger than that produced by single field”
Define the degeneracy factor that is equal to the number of distinct permutations of the applied field
NO

## Slide 35: Degeneracy Factor and Third-order Susceptibility
Considering with degeneracy factor D
Third-order susceptibility
Considering with degeneracy factor that represents the number of distinct permutations of the frequencies

## Slide 36: 1.4 Nonlinear Susceptibility of a Classical Anharmonic Oscillator

## Slide 37: E-field of the Frequency Components
Lorentz model of the atom
It provides a good description of the linear optical properties of atomic vapors
The Lorentz model treats the atom as a harmonic oscillator
Nonlinearity of Lorentz model of the atom
Extending the restoring force
The details of the analysis differ depending upon “inversion symmetry of the medium”
Defect of Lorentz model
A single resonance frequency to each atom : only one resonance frequency
In quantum-mechanical theory, it allows each atom to possess many energy eigenvalues and hence than one resonance frequency

## Slide 38: Noncentrosymmetric Media
For noncentrosymmetric medium (electron position : )
: applied E-field, : the charge of the electron and damping force :
Restoring force : assuming that it is a nonlinear function of the displacement of the electron
Potential energy
F. Ding et al., Inorg. Chem. 57, 7950 (2018).
: parameter about the strength of the nonlinearity
Anharmonic correction
Even and odd powers of
Not perfectly parabolic
Scalar-field approximation : cannot treat the tensor of the nonlinear susceptibility without assumption about symmetry
https://opengeology.org/Mineralogy/10-crystal-morphology-and-symmetry/

## Slide 39: Perturbation Expansion Approach
Potential energy for a noncentrosymmetric medium
Assuming that the applied is sufficiently weak :
Assuming the applied optical field
Can be solved by means of a perturbation expansion
Input when finishing calculation
A solution is the form of a power-series expansion in the

## Slide 40: Perturbation Expansion Approach
(linear) Lorentz model
Steady state solution in (linear) Lorentz model

## Slide 41: Perturbation Expansion Approach
The square of contains several frequencies
Choose the response at frequency for instance,
Steady state solution
and
Another examples,

## Slide 42: Linear Susceptibility
Linear susceptibility ()
Close to resonance
Number density of atoms
FWHM
Atomic absorption
profile
Resonance

## Slide 43: Nonlinear Susceptibility
Nonlinear susceptibility ()
In terms of the product of linear susceptibilities
Number density of atoms
Second-order susceptibility as a function of three frequencies
For SFG case, one () of the fields goes and DFG case, Optical rectification () case are
If you want to know susceptibility, you should expand

## Slide 44: Miller’s Rule
Empirical rule due to Miller
Nearly constant for all noncentrosymmetric crystals
Nearly constant
Atomic number density : for all condensed matter and are constant
The size of the nonlinear coefficient by the linear and nonlinear contributions to the restoring force
Assuming that size of the atom (separation between atoms; lattice constant )
This reasoning leads to the order-of-magnitude estimate
Roughly the same for all materials
By reasons of nonsymmetry,

## Slide 45: Nonlinear Coefficient
The estimate of nonlinear coefficient
To estimate of the size of the second-order susceptibility under highly nonresonant conditions

## Slide 46: Centrosymmetric Media
Electronic restoring force for centrosymmetric medium
: the strength of the nonlinearity (usually positive value)
Symmetry under the operation :
Assuming that the electronic displacement never becomes so large
F. Ding et al., Inorg. Chem. 57, 7950 (2018).
A center of inversion symmetry
lowest-order correction
Nonlinear term contributes to third-order polarization as a susceptibility
Cannot be specified unless the internal symmetries of the medium are completely known
Assuming that a material is isotropic
For examples, glasses and liquids
https://opengeology.org/Mineralogy/10-crystal-morphology-and-symmetry/

## Slide 47: Equation of Motion for Isotropic Material
The equation of motion for the isotropic material
Assuming the input field has three distinct frequency components (for three-order interaction)
If anharmonics term is very weak, we can also use perturbation
As in the previous case about ,

## Slide 48: Linear Susceptibility
Steady-state solution
The Cartesian components of the polarization
Principal axes in linear susceptibility
The second-order response is not driven,

## Slide 49: Third-order Response
Third-order response
Let these frequencies be

## Slide 50: Third-order Response (cont.)
Third-order nonlinear susceptibility
Linear susceptibility has only principal axes
Intrinsic permutation symmetry : Six possible permutations
So, we define one-six of the sum of the six expression

## Slide 51: Estimate Nonlinear Coefficient
Estimate nonlinear coefficient
The linear and nonlinear contributions to the restoring force will become comparable in magnitude
Atomic dimension
For nonresonant excitation,

## Slide 52: 1.5 Properties of the Nonlinear Susceptibility

## Slide 53: Estimate Nonlinear Coefficient
Symmetry properties
Considering the mutual interaction of three waves of frequencies
We should know nonlinear polarization for a complete description
Six tensor quantities of positive frequency
In Cartesian system,
So, If we don’t have any information about symmetry, we must know complex components of 324 to describe the interaction
Fortunately, there are a number of restrictions resulting from symmetry

## Slide 54: Reality of the Fields
Real value of polarization & susceptibility
Purely real : physically measurable
We can directly obtain the negative frequency quantity from positive thing

## Slide 55: Intrinsic Permutation Symmetric
Intrinsic permutation symmetric
Physically same quantities
So, must be equal to
this condition is simply a statement that it cannot matter which is the first field and which is the second field in products
For dummy indices,
Note that this symmetry condition is introduced purely as a matter of convenience.

## Slide 56: Symmetry for Lossless Media
Two additional symmetries of the nonlinear susceptibility tensor
Fully permutation symmetry
All of the frequency arguments of the nonlinear susceptibility can be freely interchanged, as long as the corresponding Cartesian indices are interchanged simultaneously
Assuming that our frequencies are far from resonant frequency
Susceptibility goes real
Example of two conditions

## Slide 57: Field Energy Density for a Linear Medium
Full permutation symmetry from EM-field energy
Full permutation symmetry of susceptibility is deduced from EM field energy within a nonlinear medium
Energy density according to Poynting’s theorem within a linear medium,
Displacement vector & dielectric tensor
Energy density
In vacuum
Polarization of the medium

## Slide 58: Field Energy Density for a Nonlinear Medium
Full permutation symmetry from EM-field energy
Energy density according to Poynting’s theorem within a nonlinear medium,
as coefficients in the power series expansion of
The polarization of a medium is given by the expression
General form is
The order of Multiplied E-fields is not immaterial, so, the quantity is full permutation symmetry

## Slide 59: Field Energy Density for a Nonlinear Medium
Linear and nonlinear polarization
Linear polarization
Nonlinear polarization
Sign of first frequency
possesses full permutation symmetry, so does.

## Slide 60: Supple : calculate the polarization
Linear polarization
Nonlinear polarization

## Slide 61: Kleinman’s Symmetry
Nonresonant case under the low-frequency excitation
Quite often, in nonlinear optical interactions
The system responds instantaneously to the applied field
Optical waves () are much smaller than the lowest resonance frequency of material system
Susceptibility is essentially independent of frequency
Full permutation symmetry is valid under our circumstances
But, susceptibility doesn’t depend on the frequencies
Kleinman symmetry condition : no dispersion of the susceptibility

## Slide 62: Contracted Notation
Introducing notation when the Kleinman symmetry condition is valid
The tensor
Nonlinear polarization
Assuming that is symmetric in its last two indices
Nonlinear susceptibility tensor : matrix
Just convention
Valid whenever Kleinman’s symmetry condition is valid
Generally, it is valid for SHG

## Slide 63: Contracted Notation
Introducing notation when the Kleinman symmetry condition is valid
Not all of the 18 elements are independent under the Kleinman symmetry condition
Only 10 independent elements
The nonlinear polarization leading to SHG

## Slide 64: Contracted Notation
Introducing notation when the Kleinman symmetry condition is valid
The nonlinear polarization leading to SFG

## Slide 65: Effective Value
Nonlinear polarization for a fixed geometry (propagation direction and polarization)
It is possible to express the nonlinear polarization (SFG and SHG)
is obtained by determining in matrix equation and then calculating its norm
For example, negative uniaxial of crystal class 3m (as type II condition)
Midwinter, J.E., Warner, J., 1965. Br. J. Appl. Phys. 16, 1135.

## Slide 66: Effective Value
Nonlinear polarization for a fixed geometry (propagation direction and polarization)
Midwinter, J.E., Warner, J., 1965. Br. J. Appl. Phys. 16, 1135.
For example, negative uniaxial of crystal class 3m (as type II condition)
: the angle between the propagation vector and the crystalline axis (the optic axis)
: the azimuthal angle between the crystalline axis and the projection for the propagation vector onto the crystalline plane

## Slide 67: Spatial Symmetry of Nonlinear Medium
Fourfold axis of symmetry
The linear and nonlinear susceptibility tensors are constrained by the symmetry properties of the optical medium.
If the crystal were rotated by 90 degrees about the z axis, crystal structure would look identical.
Nonlinear polarization for a fixed geometry (propagation direction and polarization)
The linear and nonlinear optical susceptibilities
mathematical method (group theory)
determined by symmetry properties
What types of symmetry properties can occur in a crystalline medium

## Slide 68: Spatial Symmetry of Nonlinear Medium
Crystal Classification by group theory
32 possible crystal classes depending on the point group symmetry of the crystal
Fourfold axis of symmetry : point group 4
Three-fold axis of symmetry and a plane of mirror symmetry parallel to this axis : point group 3m
https://opengeology.org/Mineralogy/10-crystal-morphology-and-symmetry/
R. Ballou, Crystallography: Symmetry groups and group representations, Eur. Phys. J. Conf. 22, 00006 (2012).

## Slide 69: Influence of Spatial Symmetry
Considering symmetry imposes on the linear susceptibility tensor
Five difference cases by a group theorical analysis
Isotropic materials are also included in below table
Isotropic crystal : only diagonal with equal diagonal components
Anisotropic crystal : polarization needs not to parallel to E-field (Birefringence)
Tetragonal, Trigonal, Hexagonal crystal : uniaxial crystals
Rotational symmetry
Biaxial crystals

## Slide 70: Influence of Spatial Symmetry
Crystals are categorized seven possible crystal systems
32 point group

## Slide 71: Influence of Spatial Symmetry (Nonlinear Response)
Centrosymmetry (inversion symmetry)
must vanish
11 of the 32 crystal classes : inversion symmetry
Proof why inversion symmetry vanish second-order susceptibility
Assuming medium that responds instantaneously to the applied optical field
then by inversion symmetry
Must be same :

## Slide 72: Influence of Spatial Symmetry (Nonlinear Response)
Intuitively by considering the motion of an electron in a nonparabolic potential well
: no distortion
: odd harmonics; time-averaged response is zero
: even and odd harmonics; time-averaged response is not zero

## Slide 73: Influence of Spatial Symmetry (Nonlinear Susceptibility)
For example, here’s a crystal of class 3m
matrix
Caution : considerable spread in the values of the nonlinear coefficients
Because of the wavelength dependence of the nonlinear and measurement inaccuracies
Kleinman symmetry is also involved

## Slide 74: Number of Independent Elements of Susceptibility
How to reduce the elements
for describing mutual interaction of three optical waves
Physical fields (polarization, E-field) are real
Intrinsic permutation symmetry (about input fields)
lossless medium (real susceptibility) and full permutation symmetry
For SHG
Kleinman’s symmetry (low-frequency excitation)
Frequency indices + E-field indices : simultaneously
Considering input fields

## Slide 75: Noncentrosymmetric and Cubic Crystal Classes
A material can possess a culbic lattice and be noncentrosymmetric
Gallium arsenide : structure as the zincblende
Its point group : : nonvanishing second-order nonlinear optical response
noncentrosymmetric
Not zero
cubic lattice (isotropic)
Cubic lattice : Gallium arsenide doesn’t display birefringence
Hard phase-matching
Birefringence is commonly used to achieve phase-matching
But cubic lattice is isotropic, it is too hard to achieve it

## Slide 76: Noncentrosymmetric and Cubic Crystal Classes
Different nearest-neighbors give different characteristic
Diamond structure : cubic lattice and centrosymmetric
Zincblende structure : cubic lattice and noncentrosymmetric

## Slide 77: Noncentrosymmetric and Polar Crystal Classes
Restrict condition that possess a nonzero second-order susceptibility
Certain crystal possess a permanent dipole moment
Polar crystals, ferroelectric crystals
They can display the pyroelectric effect and photorefractive effect
A change of permanent dipole moment with temperature
which can be used to construct optical detector
Ferroelectric crystals within group theoretical arguments
Polar crystals
Noncentrosymmetric crystal
Always Yes!
Always No!
For example, cannot posses a permanent dipole moment. But it is noncentrosymmetric

## Slide 78: Third Order Nonlinear Response
Pass

## Slide 79: Time-Domain Description of Optical Linearities
Describing optical nonlinearities directly in the time domain
Sometimes more convenient than frequency domain (Short pulse applied field)
A purely linear response
: linear response function
Frequency domain is useful when input field is nearly monochromatic
Contribution to the polarization produced at time by an E-field applied at earlier time
Low limit of integration is 0 by causality : depends only on past
Transformed to the frequency domain (FT)

## Slide 80: Time-Domain Description of Optical Linearities
FT of the polarization & linear susceptibility
Polarization of linear response

## Slide 81: Time-Domain Description of Optical Nonlinearities
FT of Second-order response function
if either or is negative
Third-order

## Slide 82: Kramers-Kronig Relation
Kramers-Kronig (KK) relations
These condition relate real and imaginary parts of frequency-dependent quantities
A knowledge of the frequency dependence of the imaginary part → the real part of the susceptibility at some frequency
Measuring an absorption spectrum : easier than to measure the frequency dependence of the refractive index

## Slide 83: Kramers-Kronig Relation in Linear Optics
Kramers-Kronig (KK) relations in linear optics
: polarization and applied field is real quantities
is analytic (single valued and possessing continuous derivatives)
in the upper half of the complex plane :
for convergence
: must be square integrable; is physically measurable quantity

## Slide 84: Kramers-Kronig Relation in Linear Optics
Cauchy principal value of the integral
Considering the integral with simple pole
Desired integral
Cauchy principal value of the integral
: closed path
:
Integrand
Finite response time
Residue theory

## Slide 85: Kramers-Kronig Relation in Linear Optics
Cauchy principal value of the integral
It is usually easier to measure absorption spectra than the frequency dependence of the refractive index